## Slide 1: Computer Organization and Architecture Exp 2 Serial Adder & Parallel Adder
Notes: OK,now it’s the second experiment of our class, this experiment’s topic is SAPA.

## Slide 2: Preface
Experiment Purpose
  (1) Understand the sturcture of serial and parallel adder;
  (2) Know the principle and implementation of arithmetic shift register;
Experiment content
  Design 4-bit signed serial adder and parallel adder with same inputs, and compare the resuts of them.

## Slide 3: 1 Understanding
HA(Half-Adder) FA(Full-Adder)
Input
Sum
Carry
HA
HA
Input
Output
Si = Ai⊕ Bi⊕Ci
Ci+1=Ai·Bi+(Ai ⊕Bi)·Ci
Notes: At first , we need to understand the principle of HA & FA. (Small pause) the HA has 2 inputs of A & B

## Slide 4: 2.1Design for Serial-Adder
B’n-1
B’n-2
B’1
A0
Fn-1
OF
M=1Sub
C0
C1
C2
Cn-2
Cn-1
Cn
FA
FA
FA
FA
Bn-1
An-1
Bn-2
An-2
A1
B1
B0
……
…………
Sign bit
M=0Add
Op-control M
……
Fn-2
F1
F0
B’0
An-1 and Bn-1 are sign bits ，Overflow Flag：OF ＝ Cn ⊕ Cn-1
[A]补=An-1An-2…A1A0 [B]补=Bn-1Bn-2…B1B0
Fi = Ai⊕ Bi⊕Ci Ci+1=Ai·Bi+(Ai ⊕Bi)·Ci
Notes: 补码的加法计算器

## Slide 5
[A]补=An-1An-2…A1A0 [B]补=Bn-1Bn-2…B1B0
Fi = Ai⊕ Bi⊕Ci Ci+1=Ai·Bi+(Ai ⊕Bi)·Ci
[B]补=Bn-1Bn-2…B1B0
Ai⊕ Bi
Ai·Bi
(Ai ⊕Bi)·Ci
Fi = Ai⊕ Bi⊕Ci
Ci+1=Ai·Bi+(Ai ⊕Bi)·Ci
An-1An-2…A1A0 Bn-1Bn-2…B1B0
Notes: 减去一个数，等于加上这个数的补码（减去一个数，等于加上他的相反数的补码）
负数的补码等于原码取反加一（符号位不取反）， m=1,B经xor取反，并加上1(即m)得其补码

## Slide 6: 2.2 Design for Parallel-Adder
C1=Y0+X0C0
C2=Y1+X1C1 =Y1+X1Y0 +X1X0C0
C3=Y2+X2C2=Y2+X2Y1 +X2X1Y0 +X2X1X0C0
C4=Y3+X3C3=Y3+X3Y2 +X3X2Y1 +X3X2X1Y0 +X3X2X1X0C0
Let Yn= An·Bn Xn= (An⊕Bn)
Cn+1=Yn+XnCn
Yn is the carry bit generation function of 4-bit carry addition chains.
Xn is the carry bit transition function of 4-bit carry addition chains.
Ci+1 =Ai ·Bi + (Ai ⊕Bi )·Ci

## Slide 7
C1=Y0+X0C0
C2=Y1+X1C1
=Y1+X1Y0 +X1X0C0
C3=Y2+X2C2
=Y2+X2Y1 +
X2X1Y0 +X2X1X0C0
C4=Y3+X3C3
=Y3+X3Y2 +X3X2Y1
+X3X2X1Y0 +X3X2X1X0C0
Notes: 最高位得进位输出不等于最高位得进位输入，则发生溢出

## Slide 8: The whole diagram
You can find it in our experiment pdf file

## Slide 9: 3.Experiment Steps
Based on previous diagrams and principles, design the whole circuit diagram and verify the correctness.
Start the simulation, Switch SW2 to make 1. Let BUS_[7..4]=0101，BUS_[3..0]=0010(Set the input bits in DSW1)，M=0(switch SW7). Observe the result and compare it between serial and parallel adder, check if it’s overflow. If BUS_[3..0]=0011, what’s the result?
Do the same when
  BUS_[7..4]=0101，BUS_[3..0]=0011，M=1
  BUS_[7..4]=0011，BUS_[3..0]=0101，M=1
  BUS_[7..4]=1101，BUS_[3..0]=0011，M=0
  BUS_[7..4]=1101，BUS_[3..0]=0011，M=1

## Slide 10: Questions
1. Is this experimental ALU original form or 2’s complement form? Assume we want to modify the circuit into unsigned 4-bit original form ALU, what we need to do?
2. In this experiment, what’s the range of the 4-bit 2’s complement code? If we want to modify it into 5-bit 2’s complement ALU(1 bit for sign bit, 4 bits for numbers), how does the range change? How to modify it?