## Slide 1: Computer Organization and Architecture Exp 6 Micro-Controller

## Slide 2: Preface
Experiment Purpose
  (1) Understand the concept of “micro-program”, know the “instruction-microinstruction-microcommand” style of micro-program structure
  (2) Master the organization structure and design method of micro-controller.
  Experiment content
  Design a minimum prototype of CPU: generate the schemed CPU time sequence with sequence generator, and use the autocontrol of micro-controller to achieve the particular CPU function ——Program Jumping.

## Slide 3: Instructions
NOP
000 | XX | XX
HLT
111 | XX | XX
JMP1
001 | XX | XX
JMP2
addr1
010 | XX | XX
addr1
No operation
Halt
Direct addressing: addr1->PC
Indirect addressing: addr2=[addr1],addr2->PC

## Slide 4: Experiment Program (Store in PROGRAM module)
Assembly statement | Comment | (M address: machine instruction)
JMP1, 06H | Jump to 06H to execute the instruction there | 00H:00100000
 |  | 01H:00000110
HLT | Halt | 02H:11101010
NOP/Addr | No operation/Address | 03H:00001010
NOP | No operation | 04H:00000000
NOP | No operation | 05H:00000000
NOP/Addr | No operation/Address | 06H:00000010
HLT | Halt | 07H:11100001
JMP2, [06H] | Jump to 06H and execute [06H]=02H | 08H:01000000
 |  | 09H:00000110
 | Undefined | 0AH:11111111
 |  | 0BH:11111111

## Slide 6
Program module to store the program
AR_CLK to load to AR(T1)
PC_CLK to make PC increase(T2)
PC register
Address register
Instruction register
BUS data LED monitor.
The 8-bits can be data or instruction code
IR_CLK to load BUS’s data to IR (T2)
Data path
circuit

## Slide 7
 |  | Valid micro-operation signal | Function
Instruction flow ROMIR | T1 | #OE, AR_CLK（LDAR） | PCAR, ROMBUS
 | T2 | #OE, IR_CLK (LDIR), PC_CLK (PC_INC) | BUSIR, PC+1
dataflow ROMPC | T1 | #OE, #LDPC, AR_CLK (LDAR) | PCAR, ROMBUS
 | T2 | #OE, #LDPC, PC_CLK (PC_INC) | BUSPC
ROMIR
ROMPC
ROMIR
ROMIR
ROMIR
ROMPC
ROMPC
HALT
JMP2
NOP
HLT
JMP1
Instruction
Execute cycle
Fetch cycle

## Slide 8: Data path micro-operation signals
Enable signal | Function | Edge-trigger signal | Function
 | Read data from PROGRAM | / | /
 | load PC | / | /
LDAR | laod AR | AR_CLK=LDAR·T1 | →AR
LDIR | laod IR | IR_CLK=LDIR·T2 | →IR
PC_INC | PC increase by 1 | PC_CLK=PC_INC·T2 | PC+1/→PC
Enable signal | Function | Edge-trigger signal | Function
 | Read data from PROGRAM | / | /
 | load PC | / | /
LDAR | laod AR | AR_CLK=LDAR·T1 | →AR
LDIR | laod IR | IR_CLK=LDIR·T2 | →IR
PC_INC | PC increase by 1 | PC_CLK=PC_INC·T2 | PC+1/→PC

## Slide 9
Halt logic
CLOCK to control the Tx cycle

## Slide 10
【T1】ROMBUS
【T2】BUStarget(PC¦IR)
【T3】Fetch micro-address
【T4】If P1=1,jump to next micro-address
State machine of micro-instruction
micro
command
Micro
instruction
Micro
program
CPU
instruction
Micro-instruction cycle
(machine cycle)
Instruction cycle
Clock(Tx) cycle
Principle of micro-program
Machine cycle
(Execution)
Machine cycle
(Fetch instruction)
Machine cycle
(Execution)
Instruction cycle 1
Instruction cycle 2

## Slide 11
Address jump logical circuit
MROMx store the micro-instruction code
When in T1 cycle, MARx fetch the micro-instruction code and keep the output in subsequent Tx cycles.

## Slide 12
Horizontal micro-instruction format
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
·
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
LDAR
PC_INC
OE
LDIR
P1
uA4 uA3 uA2 uA1 uA0
Micro-command segment
U-address
1
LDPC
Micro-instruction code table
Addr | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
00000 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
00001 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
00010 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
00111 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Every bit of micro-command is micro-operation signal, some is defined like LDPC, LDAR, etc. Set “1” to enable, “0” to block.

## Slide 13: Address jump logical circuit.2
When P1=1,(which means fetching the instruction from IR)
load the next IR to Max in T4 cycle
Send next IRx to MROM when in T3.
Input
Output

## Slide 14
Micro-program workflow
Fetch instruction
Execute
instruction
P1 ( 0 0 I7 I6 I5 )
【T1】PCAR,ROMBUS
【T2】BUSIR, PC+1
00000
00000
00001
00010
00001
00000
【T1】PCAR,ROMBUS
【T2】BUSPC
【T1】PCAR,ROMBUS
【T2】BUSPC
P1( 0 0 I7 I6 I5 )
【T1】PCAR,ROMBUS
【T2】BUSIR, PC+1
HALT
00000
00000
00111
P1 ( 0 0 I7 I6 I5 )
【T1】PCAR,ROMBUS
【T2】BUSIR, PC+1
【T1】PCAR,ROMBUS
【T2】BUSPC
00000
00000
00000
00001
NOP/HLT(I7I6I5 =000/111)
JMP1(I7I6I5 =001)
JMP2(I7I6I5 =010)
start
end

## Slide 15
Address jump
Logical circuit
OP code
Address register
Address decode
Control ROM
(MROMx)
P1, P2
Micro-command segment
……
Micro-Operation signal
IR
…
State condition
Micro-instruction register
Micro-program structure

## Slide 16: Experiment Steps
Exp1: JMP1 and JMP2
  According to the code below, compile and make the hex files and burn them into EPROM1、EPROM2、EPROM3 seperatively(WARNING: DO NOT MESS IT).
EPROM1 | EPROM2 | EPROM3
ORG 0000H DB 00000001B DB 00000001B DB 00000001B DB 00000000B DB 00000000B DB 00000000B DB 00000000B DB 00000000B END | ORG 0000H DB 00100101B DB 10100100B DB 10100100B DB 00000000B DB 00000000B DB 00000000B DB 00000000B DB 00000000B END | ORG 0000H DB 01000000B DB 00000000B DB 00000001B DB 00000000B DB 00000000B DB 00000000B DB 00000000B DB 00000000B END
Question: In the micro-instruction table, [00001] and [00010]’s operation
is completely same.So, can we merge these two instructions? If not,why?

## Slide 17
Compile the code below and burn it into PROGRAM module.
ORG 0000H
DB 00100000B; JMP1, 06H
DB 00000110B
DB 11101010B; HLT
DB 00001010B; NOP/Addr
DB 00000000B
DB 00000000B
DB 00000010B; NOP/Addr
DB 11100001B; HLT
DB 01000000B; JMP2, [06H]
DB 00000110B
END

## Slide 18
Before start, swtich CLK to MANUAL_CLK; Start simulation, make RESET=1, manually press MANUAL_CLK to make CLK rising-edge transit. Initial {T1,T2,T3,T4}={1,0,0,0}; MAKE RESET=0 and the initial process complete.
Press MANUAL_CLK and make CLK pulse as“ ”, step over the above program. In the instruction cycle of JMP1 and JMP2, compare to workflow of _ ,observe the function of micro-instruction and the stepping result( data of AR,IR,PC,BUS).
Switch CLK to AUTO_CLK(10hz)，the program will run to HLT break point and pause. Look into the number of micro-instruction cycles in break point and the result data of AR,IR,PC,BUS. Then enable RESET as “0->1->0”, jump out break point and run the next instruction

## Slide 19
Exp2: JMP3
  Add a new jump instruction JMP3 as below. Supply the micro-program workflow and micro-instruction code table. Implement the function of JMP3.
instruction | OP code | ML program | comment
JMP3 | 011 | 01100000; JMP3 xxxxxxxx; addr1 | Secondary indirect addressing: program jump 3 times to addr3 to excute [addr1] =addr2, [addr2]= addr3, addr3→PC;

## Slide 20
Compile the code to hex file and burn it to PROGRAM.
ORG 0000H
DB 00100000B; JMP1, 06H
DB 00000110B
DB 11101010B; HLT
DB 00001010B; NOP/Addr
DB 01100000B; JMP3, [[0BH]]
DB 00001011B
DB 00000010B; NOP/Addr
DB 11100001B ; HLT
DB 01000000B; JMP2, [06H]
DB 00000110B
DB 11100000B; HLT
DB 00000011B; NOP/Addr
END

## Slide 21
Refer to the initial process and step over method of exp1, repeat the experiment and observe the result data.
Refer to the method of auto-run and jumping out of break point in exp1, auto run the program, observe the micro-instruction cycles in break point and the data of AR,IR,PC,BUS.
Question: In this experiment’s program, some addresses is annotated as “NOP/[ADDR]”. What’s the difference of NOP and NOP/[ADDR]?
Under what situation it will do nothing or jump the program?